## Slide 1: Arduino GSM Shield
Soundararajan dhakshinamoorthy

## Slide 2: Overview
Allows you to do almost anything you do with GSM and GPRS.
Has a modem that transfer data from a Serial port to GSM Network.
The library abstracts low level communication between modem and SIM card.
Each command is part of a larger set of operations.
Internally handled by AT commands.
Utility commands available for separate use.

## Slide 3: The library overview
The GSM class takes care of commands to the radio modem. This handles the connectivity aspects of the shield and registers your system in the GSM infrastructure. All of your GSM/GPRS programs will need to include an object of this class to handle the necessary low level communication.
Voice call handling, managed by the GSMVoiceCall class.
Send/receive SMS messages, managed by the GSM_SMS class.

## Slide 4: Library overview
The GPRSClass is for connecting to the internet.
GSMClient includes implementations for a client, similar to the Ethernet and WiFi libraries.
GSMServer includes implementations for a server, similar to the Ethernet and WiFi libraries. NB : A number of network operators do not allow for incoming connections from the public internet, but will allow them from inside their own. Check with your operator to see what restrictions there are on data use.
A number of utility classes such as GSMScanner and GSMModem

## Slide 5: SendSMS
Setup PIN if needed.
Run the SendSMS.ino example.

## Slide 6: VoiceCall
Run the voicecall sketch.