## Slide 1: Arduino Types
Many different versions
  Number of input/output channels
  Form factor
  Processor
Leonardo
Due
Micro
LilyPad
Esplora
Uno

## Slide 2: Leonardo
Compared to the Uno, a slight upgrade.
Built in USB compatibility
Bugs?
  Presents to PC as a mouse or keyboard

## Slide 3: Due
Much faster processor, many more pins
Operates on 3.3 volts
Similar to the Mega

## Slide 4: Micro
When size matters: Micro, Nano, Mini
Includes all functionality of the Leonardo
Easily usable on a breadboard

## Slide 5: LilyPad
LilyPad is popular for clothing-based projects.

## Slide 6: Esplora
Game controller
Includes joystick, four buttons, linear potentiometer (slider), microphone, light sensor, temperature sensor, three-axis accelerometer.
Not the standard set of IO pins.

## Slide 7: Mega
Compared to the Uno, the Mega:
  Many more communication pins
  More memory
  Some interface hardware doesn't work

## Slide 8: Arduino Uno Close Up
The pins are in three groups:
  Invented in 2010
  14 digital pins
  6 analog pins
  power

## Slide 9: Arduino Board Overview
Microcontroller
chip
Power
pins
Digital input/output pins
Power LED
Reset button
Analog
Input
pins
Power connector
USB connector
USB chip

## Slide 10: Shields
Shields are circuit boards that plug into the top of an Arduino.
They extend the capabilities of an Arduino.
Examples:
  Ethernet
  GPS
  Motor
  Prototype
shieldlist.org

## Slide 11: Compatible Boards
These are two of MANY!
Notes: This is the Diavolino and the Ruggeduino. The Diavolino is a low cost board ($12 at Micro Center) that off-loads the USB processing to another board. It is a kit. The Ruggeduino is built for beginners and has fuses and other limiting components to nearly eliminate the possibility of damaging the board.
These are two of many. Since Arduino is open, anyone can make boards, and many have extended boards for special purposes, such as robots, flight simulation, video games, radio control vehicles, and for prototyping.

## Slide 12: Compatible Boards

## Slide 13: Shields
Notes: Shields connect to the I/O board to extend it's functionality. Hundreds of shields are available, and you can make your own.
Starting from the upper left going clockwise:
Wireless Network Shield
Color LCD Shield
Power Driver Shield (connects to a computer power supply).
GPS Shield
Shields can run as low as $15, as high as $200.
Bluetooth $40-$65
LCD: $40
GPS: $80
Power Driver: $20

## Slide 14: Shields
Touchscreen Shield
Wave Shield
Datalogging Shield
Notes: The shield on the left is a touchscreen shield, the upper right is a light and temperature shield, and the lower right is a sound (music) shield.

## Slide 15: More Shields…
Ethernet Shield
XBee Shield
Wifi Shield
Notes: Communication shields - XBee, Ethernet, and Wifi (2.5 Ghz).
These run around $60-$80.

## Slide 16: And more shields…

## Slide 17: Even more shields!
APRS Shield

## Slide 18: Modules
Bluetooth Module
GPS Module
RFID Module
Temperature & Humidity Sensor
Notes: Modules send serial data strings to the Arduino.

## Slide 19: Arduino Starter Kits
Start with a combo pack (starter kit)
  Includes a microcontroller, wire, LED's, sensors, etc.
www.adafruit.com
  adafruit.com/products/68 ($65)
www.sparkfun.com
  https://www.sparkfun.com/products/11576 ($99.95)
Radio Shack
  Make Ultimate Microcontroller Pack w/ Arduino Kit ($119.99)
www.makershed.com
  http://www.makershed.com/Ultimate_Arduino_Microcontroller_Pack_p/msump1.htm ($150)